## Slide 1: Navigation and 3D Mapping with ROS2
Michele Pestarino ()
Federico Sacco ()
Thomas Campagnolo (5343274)
Software Architectures for Robotics (A.Y. 2021/22)

## Slide 2: UML – Unified Modelling Language

## Slide 3: UML – Unified Modelling Language
Nota a piè di pagina
    Diagrammi UML

## Slide 4: Navigation2

## Slide 5: Navigation2 - Overview
https://navigation.ros.org/index.html
Autonomous mobile robot navigation framework
Behavior Tree-based navigation
Independent Modular Servers
Multiple local trajectory and path planners
Sensors processing for collision avoidance
Recovery behaviors
Positioning system
Runtime lifecycle manager
Plugins

## Slide 6: Navigation2 – Behavoir Trees (BT) Navigation
https://navigation.ros.org/index.html
Why BT?
Tree-based execution model and task planner
Set many different plugins types
Model complex tasks
Using BT
CPP library
Specific Nodes: Action, Condition, Decorator, Control
Custom nodes to extend or change behavior
  Navigate to pose
  Navigate through poses and pause near goal-obstacle
  Navigate and replan multiple path and trajectory
  Follow dynamic object
  Odometry calibration
Example BT: Navigate to Pose with Replanning and Recovery
Behavior trees XML file
BT node call task server in other processes
  Navigation subtree, Recovery subtree

## Slide 7: Navigation2 – Modular
https://navigation.ros.org/index.html
Indipendent Servers and Plugins
Map Server, load, serve, and store maps;
AMCL, localize the robot on the map;
Nav2 Planner, plan a path from A to B around obstacles;
Nav2 Controller, control the robot as it follows the path;
Nav2 Smoother, smooth path plans to be more continuous and feasible;
Nav2 Costmap 2D, convert sensor data into a costmap representation of the world;
Nav2 Recoveries, compute recovery behaviors in case of failure;
Nav2 Core, plugins to enable your own custom algorithms and behaviors;
…

## Slide 8: Spatio-Temporal Voxel Layer (STVL)

## Slide 9: STVL - Overview
https://github.com/SteveMacenski/spatio_temporal_voxel_layer/
Navigation2 Plugin
  Costmap Layer
Developed and maintained by Steven Macenski at Simbe Robotics
OpenVDB, open-source C++ library built by Dreamworks “comprising a novel hierarchical data structure and a suite of tools for the efficient storage and manipulation of sparse volumetric data discretized on three-dimensional grids...”
Tasks
- Replacement for the standard voxel representation of the environment
- Ability to efficiently maintains temporal 3D sparse volumetric voxel grid with decay through sensor models
- Wrapped with ROS tools and interfaces to the navigation stack for uses in standard ROS configurations
- Possible without ROS/Navigation

## Slide 10: Why STVL?
https://github.com/SteveMacenski/spatio_temporal_voxel_layer/
Spatio-
- representation of the environment in a configurable “voxel_size” voxel grid
- possibility of executing an approximate voxel grid filter for buffered measurements, which can be parameterized at
runtime in the configuration yamls
- reduction of spikes in the “move_base” cpu due to dense measurement readings when approaching objects
(i.e. more points)
- slightly increase overheads (1-2%) for nominal operations
-Temporal
- novel concept of “voxel_decay” with configurable functions that expire voxels and their occupation over time
- store times in each voxel after which the voxel will disappear from the map
- the time it takes to clear depends on the configured functions and acceleration factors
- voxel acceleration uses given FOV to compute the frustum geometry:
  Depth cameras (e.g. Intel Realsense) are modeled with traditional 6-planed cubical frustums
  3D lidars (e.g. Velodyne VLP 16) are modeled with their hourglass-shaped FOV.

## Slide 11: Why STVL?
https://github.com/SteveMacenski/spatio_temporal_voxel_layer/
Local Costmap
- use of the information coming from the robot before the decay time for the local cost map
- configuration of a short decay time of the voxels in order to plan only in relative space
- operate with more information than other times when the speed is faster or slower
- decay time 5-15 seconds nominally good
Global Costmap
- time of 15-45 seconds due to things moving in the scene (e.g. shop, warehouse, construction zone, office, etc.)
- possibility of not decaying the voxels in the global map
  permanent voxels set decay to -1 (not recommended for planar lidars)
Mapping
- map an environment in 3D in real-time
  mapping mode will maintain the entire voxel grid and save the map using the services provided (maps may be visualized using vdb_viewer)
- run multiple instances of the layer one to map and other to navigate

## Slide 12: Linorobot2

## Slide 13: Linorobot2 Simulation - Overview
Link alla nostra github repository
Description
Navigation and mapping with ROS 2 using the Nav2 package for robot navigation and the Spatio-Temporal Voxel Layer (STVL) plugin for mapping the explored environment in 3D.
Task
Test and explore the capabilities of this 3D mapping plugin with multiple map layouts.

## Slide 14: Linorobot2 Simulation - Overview
Didascalia delle immagini
Metterci qualche screen di linorobot all’interno dei diversi ambienti? (oppure inserirle nella slide precedente)

## Slide 15: Linorobot2 Simulation – Office Environment
VIDEO RVIZ
VIDEO RVIZ
3D LiDAR Sensor
RGB-D Sensor

## Slide 16: Linorobot2 Simulation – Office Environment
3D LiDAR Sensor
RGB-D Sensor
Breve descrizione dei topic, dimensione voxel ecc….
Analizzare le differenze
Breve descrizione dei topic, dimensione voxel ecc….
Analizzare le differenze

## Slide 17: Linorobot2 Simulation – Playground Environment
VIDEO RVIZ
VIDEO RVIZ
3D LiDAR Sensor
RGB-D Sensor

## Slide 18: Linorobot2 Simulation – Playground Environment
3D LiDAR Sensor
RGB-D Sensor
Breve descrizione dei topic, dimensione voxel ecc….
Analizzare le differenze
Breve descrizione dei topic, dimensione voxel ecc….
Analizzare le differenze

## Slide 19: Linorobot2 Simulation – 3D LiDAR vs RGB-D
3D LiDAR Sensor
RGB-D Sensor
PRO / CONTRO
PRO / CONTRO

## Slide 20: What’s Next?

## Slide 21: What’s Next?
Implementazione su altri tipi di robot

## Slide 22: Repository, Documentation and Issue
Tutti i link delle repository, documentazioni ecc… (nostra repo, nav2, STVL, …)