## Slide 1: Navigation and 3D Mapping with ROS2
Michele Pestarino (4672010)
Federico Sacco (4672032)
Thomas Campagnolo (5343274)
Software Architectures for Robotics (A.Y. 2021/22)

## Slide 2: Navigation2

## Slide 3: Navigation2 - Overview
Autonomous mobile robot navigation framework based on independent modular servers.
Behavior Tree-based navigation.
Multiple local trajectory and path planners.
Sensors processing for collision avoidance.
But also: recovery behaviors, positioning system, lifecycle manager.
https://navigation.ros.org/index.html

## Slide 4: Navigation2 - Overview
Independent Servers and Plugins
Map Server, load, and store maps
AMCL, localize the robot on the map
Nav2 Planner, plan a path from A to B around obstacles
Nav2 Controller, control the robot as it follows the path
Nav2 Smoother, smooth path plans to be more continuous and feasible
Nav2 Costmap 2D, convert sensor data into a costmap representation of the world
Nav2 Recoveries, compute recovery behaviors in case of failure
Nav2 Core, plugins to enable your own custom algorithms and behaviors
https://navigation.ros.org/index.html

## Slide 5: Spatio-Temporal Voxel Layer (STVL)

## Slide 6: STVL - Overview
Navigation2 plugin that efficiently maintains temporal 3D sparse volumetric voxel grid with decay through sensor models
Replacement for the standard voxel representation of the environment
Wrapped with ROS tools and interfaces to the navigation stack for uses in standard ROS configurations and other systems
https://github.com/SteveMacenski/spatio_temporal_voxel_layer/

## Slide 7: Why STVL?
https://github.com/SteveMacenski/spatio_temporal_voxel_layer/
Spatio-
Configurable voxel size and general appearance in rviz
Configurable max and min perceived obstacle height
Range within which obstacles are voxelized
No assumption on a static environment or map size
No maximum number of voxel height constraint
-Temporal
Configurable voxel decay time
Persistent mapping capabilities provided by service
Graphics optimization

## Slide 8: Why STVL?
https://github.com/SteveMacenski/spatio_temporal_voxel_layer/
Local Costmap
- use of the information coming from the robot before the decay time for the local cost map
- operate with more information than other times when the speed is faster or slower
- decay time 5-15 seconds nominally good
Global Costmap
- time of 15-45 seconds due to things moving in the scene (e.g. shop, warehouse, construction zone, office, etc.)
- possibility of not decaying the voxels in the global map
  permanent voxels set decay to -1 (not recommended for planar lidars)
Mapping
- map an environment in 3D in real-time
  mapping mode will maintain the entire voxel grid and save the map using the services provided (maps may be visualized using vdb_viewer)
- run multiple instances of the layer one to map and other to navigate

## Slide 9: Linorobot2

## Slide 10: Linorobot2 Simulation
https://github.com/mic-pest/SofAr_assignment/tree/master/linorobot2
ROS2 framework for simulation with the following characteristics:
  Parameterized URDF and xacro files
  SLAM features
  Nav2 integration

## Slide 11: Project Outline
  URDF files modification
    LiDAR 3D
    RGBD camera
    Sensor tuning
  SLAM features
    Maps yaml files creation
  Integration with Spatio-Temporal Voxel Layer (STVL) Nav2 plugin
https://github.com/mic-pest/SofAr_assignment/tree/master/linorobot2

## Slide 12: Linorobot2 Simulation
Foto modello robot
Screenshot mappe usate

## Slide 13: Linorobot2 Simulation – Office Environment
3D LiDAR Sensor voxel grid
3D LiDAR sensor pointcloud
Breve descrizione dei topic, dimensione voxel ecc….
Analizzare le differenze
Breve descrizione dei topic, dimensione voxel ecc….
Analizzare le differenze

## Slide 14: Linorobot2 Simulation – Playground Environment
VIDEO RVIZ
VIDEO RVIZ
RGB-D Sensor voxel grid
RGB-D Sensor pointcloud

## Slide 15: Linorobot2 Simulation – 3D LiDAR vs RGB-D
3D LiDAR Sensor
RGB-D Sensor
PRO / CONTRO
PRO / CONTRO

## Slide 16: UML – Unified Modelling Language

## Slide 17: Nav2 RQT Topic’s Graph

## Slide 18: What’s Next?

## Slide 19: What’s Next?
Implementazione su altri tipi di robot

## Slide 20: Repository, Documentation and Issue
Tutti i link delle repository, documentazioni ecc… (nostra repo, nav2, STVL, …)